## Slide 1
VELALAR COLLEGE OF ENGINEERING AND TECHNOLOGY
PRODUCT SORTING
Automatic Product Sorting System Using Arduino and RFID
TEAM CORECREW
M. Mithra • Subiksha S. • Aadhil Ahammed P. S. • Lalith P.
Department of Electrical and Electronics Engineering

## Slide 2
PROBLEM STATEMENT
Current Situation
Courier and logistics services handle parcels for different destinations. Manual sorting can cause parcels to be mixed or placed in the wrong destination section.
Problems Identified
• Manual sorting requires more time • Wrong destination placement may occur • Human errors can cause delivery delays • Large parcel volumes increase workload • Continuous manual checking requires more effort
CORECREW | EEE | PRODUCT SORTING 2

## Slide 3
PROPOSED SOLUTION & OBJECTIVES
Proposed Solution
We developed an Automatic Product Sorting System using Arduino Uno, RFID and Servo Motor. The RFID reader identifies the parcel, Arduino processes the destination, and the servo motor directs the parcel to the corresponding section.
Objectives
• Automate parcel sorting • Reduce manual effort • Reduce parcel mix-ups • Minimize sorting errors • Improve sorting efficiency • Ensure correct destination placement
CORECREW | EEE | PRODUCT SORTING 3

## Slide 4
HARDWARE COMPONENTS
Arduino Uno
Main controller
RFID RC522
Reads parcel RFID tag
RFID Tags
Unique parcel identification
Servo Motor
Controls sorting mechanism
Conveyor / Platform
Supports or moves parcel
DC Motor / Driver
Conveyor drive, if used
Power Supply
Provides electrical power
Connecting Wires
Electrical connections
CORECREW | EEE | PRODUCT SORTING 4

## Slide 5
SYSTEM BLOCK DIAGRAM
PARCEL
RFID RC522
ARDUINO UNO
DESTINATION CHECK
SERVO MOTOR
ERODE SECTION
SALEM SECTION
COIMBATORE SECTION
RFID Detection → Arduino Processing → Destination Identification → Servo Sorting
CORECREW | EEE | PRODUCT SORTING 5

## Slide 6
WORKING PRINCIPLE
1
Parcel is placed on the sorting platform.
2
RFID RC522 detects the RFID tag.
3
RFID UID is sent to Arduino Uno.
4
Arduino compares the UID with the programmed destination.
5
Arduino sends a control signal to the servo motor.
6
Servo moves the sorting mechanism toward the required section.
7
Parcel is directed to the correct destination.
8
Servo returns to the initial position.
CORECREW | EEE | PRODUCT SORTING 6

## Slide 7
RFID MAPPING & CONNECTION
Destination Mapping
Tag 1 → Erode → Position 1 Tag 2 → Salem → Position 2 Tag 3 → Coimbatore → Position 3 Replace Tag 1/2/3 with the actual RFID UIDs used in the prototype.
RC522 → Arduino Uno
SDA → D10 SCK → D13 MOSI → D11 MISO → D12 RST → D9 GND → GND 3.3V → 3.3V Servo Signal → D6
CORECREW | EEE | PRODUCT SORTING 7

## Slide 8
PROTOTYPE, TESTING & RESULT
Prototype
RFID Detection Unit ↓ Arduino Control Unit ↓ Servo Sorting Mechanism ↓ Destination Sections Add your actual prototype photographs here.
Testing
Test 1: Erode Expected: Erode section Test 2: Salem Expected: Salem section Test 3: Coimbatore Expected: Coimbatore section
Result
The prototype demonstrates automatic destination identification and servo-based parcel sorting according to the programmed RFID information. Use your actual test results and photographs before final submission.
CORECREW | EEE | PRODUCT SORTING 8

## Slide 9
ADVANTAGES, APPLICATIONS & FUTURE SCOPE
Advantages
• Reduces manual effort • Reduces parcel mix-ups • Faster sorting • RFID-based identification • Low-cost prototype • Easy to operate
Applications
• Courier & logistics centers • Warehouses • E-commerce parcel handling • Distribution centers • Automated material handling
Future Scope
• Conveyor automation • More destinations • LCD/OLED display • IoT-based tracking • Automatic parcel counting • Barcode/QR integration
CORECREW | EEE | PRODUCT SORTING 9

## Slide 10
THANK YOU
PRODUCT SORTING
Automatic Product Sorting System
TEAM CORECREW | EEE